## Slide 1
On sites with a long historical record of wavemeter data, the use of measured data is the obvious choice. However, on most locations there is no adequate history of recorded data.
The availability of data generated by global and regional wind and wave model chains have brought radical changes to the estimation procedures of extreme SWH. Models are routinely run all over the world and SWH time series for each grid point are computed and published after assimilation (analysis) of sea truth (measured) data, generally produced by satellite altimetry
1 Global/Local Weather Model. 2 Wave Generation and Propagation Model. (Wave transformation on shallow water if necessary can be added to setp 2)
Weather and wave models
Often at price!
numerical weather forecast models are now widely available,
together with long records of past analyses and forecasts:
ECMWF, NECP, State Agencies...

## Slide 2
Wave and wind Modelling
The physical processes leading to action of waves on the coast can be divided – somewhat arbitrarily, but conveniently for our purposes – into three blocks:
1 Global Weather Model Archive Data. 2 Local Area Weather Model(s). 3 Wave Generation and Propagation Model.
.
level (1) and (2) are normally is the task of national or international Meteorological organization, which provide regular forecast of sea states and store the data for reference and scientific purposes
Its is now common practice to use of data originated from such wave models.
Global or regional wave datasets are provided by different organizations, i.e.
ECMWF (European Centre for Medium-Range Weather Forecasts)
NOAA (National Oceanic and Atmospheric Administration).

## Slide 3
wind
Assimilation
(Wind, Temperature,
Pressure etc)
HOW IS WAVE FORECAST CARRIED OUT ?
Weather
Forecast
Weather Model(s)
(Global and Regional)
Assimilation
(Wave height,
Period, spectrum etc)
Wave forecast
Wave Model(s)
(Global, Ocean, Regional)
Analysis
Re-Analysis
Wave Archives
METEO (VERY SIMPLIFIED)
WAVE(SIMPLIFIED)

## Slide 4
assimilazione
1
2
3
6
12
24
Previsione 1h
Anailisi (6 h)
To the wave model
WIND – WAVE MODELLING DATA FLOW
A TYPICAL PROCEDURE
METEOROLOGY

## Slide 5
Analysis: They aim to reproduce the real state of the athmosphere or the sea
They are issued 4 times per day: 00:00; 06:00; 12:00 e 18:00.
Forecasts Sono produced with various time time-steps (1h, 3h) and extend to up to 10 days from the generation (In Europe generally they are only issued for 3 days). Issue 2 of 4 times a day, by making use of the analysis data
Re-analysis : They are produced by reprocessing all the analysis and Forecast data , by introducing further sea ttuth information (Mostly: satellite )The are normally available with a delay of a few months
Forecast, analysis and re-analysis

## Slide 6
WAVE MODELS
Waved generation model are based on the computation of the wave spectrum :
The sea surface is covered by a computational grid; for each hpoint (x,y) and for each time t , for each frequency
σ ( =2π/T), for each direzione θ a component of the directional energy spectrum E(x,y,t; σ,θ) must be computed
Through a balance equation…
Way too complex and specialized for this course! .
If interested, see for instance:
P. Janssen “The Interaction of Ocean Waves and Wind”, Cambridge University Press, 2004.

## Slide 7
The quality of the results depends on a wide numbers of factors. Even the concept itself of the Models Sytem varies enormously: e.g., the meteorological part may be global or regional with possibly various level of nesting within the global framework; the computational grid of the wave model while obviously following the Meteorlogical structure, may be further divided into finer resolution sub-areas; assimilation of in situ data, calibration and validation may be carried out in various ways.
Spatial grid resolution of both WaN and WaM has been improving for many years due to the advances in technology, to the point that modern local models provide a resolution of a few miles, which can realistically be considered the maximum practically attainable.

## Slide 8
ECMWF
ERA
NOAA
NCEP
ECMWF
Analysis
DHI
Metoffice UK
Nettuno
Oceanweather
Deutscher
Wetterdienst
COSMO
Coupled
Uncoupled
Assimilation
Calibration
Global
Regional
WAM
WAVEWATCH SWAN
There is a zoo of models, with a whole biodiversity of options

## Slide 9
This is a typical local computational “grid”.
In any case, you end up with MILLIONS of equations

## Slide 10
Long wave records are usually kept and distributed as files which report the important parameters of each sea state: Hs, Tm, DIRection. There is of course much more information which we cannot discuss in this course

## Slide 12
FOR INSTANCE :
The NOAA National Centers for Environmental Prediction (NCEP) developed the Climate Forecast System (CFS), a fully coupled model representing the interaction between the Earth's atmosphere, oceans, land and sea ice. A reanalysis of the sea and atmosphere state for the period of 1979-2009 has been conducted, resulting in the CFS Reanalysis (CFSR) dataset (Saha, 2010). Using the CFSR dataset, the NOAA Marine Modelling and Analysis Branch (MMAB) has produced a wave hindcast for the same period by making use of the WAVEWATCH III (WW3) model (v3.14)
.
The ECMWF produced the ERA-Interim, another global atmospheric reanalysis dataset

## Slide 13
Data sources for numerical wave models
http://www.ecmwf.int/
http://www.meteoam.it/?q=cnmca
Centro
Nazionale di
Meteorologia e
Climatologia
Aeronautica
Similitudini tra i due modelli:
1) Entrambi i Centri usano per le onde un WAM;
2) Identica struttura spettrale in termini di frequenza e direzioni
Differenze sostanziali:
1) I venti utilizzati sono generati da modelli atmosferici differenti;
2) Diversa risoluzione spaziale
Modelli spettrali di III generazione:
WAM (WAMDI Group 1988, Komen et al. 1994)
WAVEWATCH III (Tolman 1997, 1999, 2009) by NOAA/NCEP
SWAN by Delft University of Technology http://www.swan.tudelft.nl/
Wind data derive frmo meteorological models

## Slide 14
MARS (Meteorological Archival and Retrieval System) of ECMWF
Forecast and Analysis
Re-analisi: .

## Slide 15
Il sito dell’ECMWF