## Slide 2
Sea wave measurement by radar systems: basic principles for maritime engineers
Misura delle onde marine con sistemi radar: principi di base perGLI INGEGNERI MARITTIMI
Eugenio Pugliese Carratelli1, Giovanni Ludeno2, Fabio Dentale1, Angela Di Leo1
1 MEDUS Department of Civil Engineering, University of Salerno 2 CNR IREA Naples

## Slide 3
1) General ideas and a few definitions
2) High incidence angles (grazing) MW: land, ship, platform based systems
3) Low incidence angles MW: satellite altimeter, SAR
4) HF radar
A lot of work has been done, including excellent tutorials on the subject.
Rossi, G.B.; Cannata, A.; Iengo, A.; Migliaccio, M.; Nardone, G.; Piscopo, V.; Zambianchi, E. Measurement of Sea Waves. Sensors 2022, 2
Eugenio Pugliese Carratelli, Giovanni Ludeno, Fabio Dentale, Angela Di Leo. Sea wave measurement by radar systems ICIRBM 2023
Ocean Wind and Wave Measurements Using X-Band Marine Radar: A Comprehensive Review Weimin Huang * ID , Xinlong Liu ID and Eric W. Gill
Some references on the paper
What is it all about?

## Slide 4
General principles- The incidence angle
α
ϑ
Angle of incidence α
α
E/M wave
Grazing angle.
Local Incidence angle ϑ
=α+ local surface slope
Fraction of local backscattered EM energy σl (ϑ), aka NRCS, «radar section»

## Slide 5
Local tilt influences σl
Whitecapping and Ko influence σl
Orbital Velocity Influences Ko
“Hydrodinamic Modulation”
Wind influences surface roughness Ko
Ko f( ϑ)
Conceptually, the main factors are:
Rough Surface :scatters
Smooth Surface: (mostly) reflects
σl depends
fundamentally on the
incidence angle
Bragg effect plays a role
For low ϑ- but not in the same way
as in HF (micro, not macro)
HH, HV, VV…

## Slide 6
Tilt φ
… and if our resolution is small enough, we see :
Local (“ a few Pixels”) variations («modulation») of σl - connected to wave agitation
Thus we get an image of the wave field
So σl varies along the surface…

## Slide 7
σo
Depends or mainly (not only) on
Roughness & whitecapping
And therefore, basically, on Wind.
(see later: satellite altimetry)
Or else…
If we see an average on “many pixels” σl
We get an average backscattering coefficient σo
Tilt φ

## Slide 8
Band | Frequency | Wavelength
Ku | 12-18 GHz | 1.67-2.5 cm
X | 8-12 GHz | 3.7-2.5 cm
C | 4-8 GHz | 3.75-7.5 cm
S | 2-4 GHz | 7.5-15 cm
----- | ----- | -----
HF 3-30 MHz 10-100 m
What is the difference?
Why is it important
Microwave Systems
vs
High Frequency
Compare
EM and sea wave length
Interacts with
sea waves
Interacts with
foam & ripples
Chart: 

## Slide 9
Microwave Systems can be either
Satellite based (Low incidence, near vertical)
or
ship or platform based (Grazing angle)
High Angle of Incidence
(grazing)

## Slide 10
Tilt φ
Local (“ a few Pixels”) variations («modulation») of σl are connected to wave agitation
we get an image of the wave field
As we saw if our resolution is small enough (and it is for MW

## Slide 11
Ϭl generates an image I
(in polar coordinates: I(r,ϑ) )
A typical microwave image of a sea wave field
Thus we do get an image, in polar coordinates
So, apparently
We could easily reconstruct the information we want, i.e. the spectrum (in wavelength and period; SWH)

## Slide 12
The instruments of darkness tell us truths,
Win us with honest trifles, to betray 's in deepest consequence.
(Shakespeare, Macbeth)

## Slide 13
Unfortunately
The image I(r,ϑ) is indeed related to the sea elevation η(r,ϑ) but it is not the same thing !
As seen earlier on, the backscattered energy I(r,ϑ) depends on various physical phenomena, such as on the slope of the waves and the roughness of the riding ripples, rather than on the water elevation η itself.
The transformation from I(r,ϑ) to η(r,ϑ) is called «modulation»

## Slide 14
We need a map of the water profile η(r,ϑ) – and of its changes with time η(r,ϑ,t)
A connection can be made between I (r,ϑ,t) and η(r,ϑ,t), or rather between their Fourier transforms: Image spectrum and Wave spectrum
= MTF
MTF is called Modulation Transfer Function. It is basically empirical. A number have been tested and applied. It must be calibrated for the particular situation.
This assumes that the connection between I and η be linear – and universal too!
the specific location, antenna, height, etc

## Slide 15
So, conceptually, the procedure goes like this
FFT of image I(ρ,ϑ,t) produces radar image spectrum
radar image transform is turned into Wave spectrum
by multiplying by Modulation Transfer Function
= MTF
From global parameters such as SWH, ωp can be extracted and if necessary a map of η can be produced
And yes, this could be done in space coordinates only, with a single Image, but the quality would be very bad indeed
This requires a succession of Images in time I(ρ,ϑ,t) . And this in turn implies a fast enough rotation of the antenna
Serafino, Ludeno, et al.
Numerous papers

## Slide 16
Filtering data through
d depth, U current
This implies excluding all the information that does not comply with the dispersion equation of water waves, thus improving the quality of the results (Signal/Noise)
Ludeno, G., Reale, F., Dentale, F., Carratelli, E.P., Natale, A., Serafino, F. Estimating
Nearshore Bathymetry from X-Band Radar Data (2015) Coastal Ocean Observing Systems,
There are ways to improve the analysis:
1) Filtering through
2) “Shadowing” (of which more in the following)
3) Doppler effect (about which more in the following)
If U, d are not known, their values can be estimated with an optimization procedure
We basicall tell the algorithm:
we only want hydrodinmically
compatible waves

## Slide 17
2D Directional Spectrum retrieved from the wave radar system
Incident wave
Reflected wave
Ludeno, G., Brandini, C., Lugni, C., Arturi, D., Natale, A., Soldovieri, F., ... & Serafino, F. (2014). Remocean system for the detection of the reflected waves from the costa concordia ship wreck. IEEE Journal of Selected Topics in Applied Earth Observations and Remote Sensing, 7(7), 3011-3018.
Wave elevation sequence
It works even in complex situations

## Slide 18
A possible improvement is the partitioning of the radar scene into sub areas,
in order to gather spatial information. Which leads to something like this
(From Ludeno, Serafino et al.)

## Slide 19
The spatial partitioning obtained with partial overlapping of two consecutive sub-area
Block diagram of novel data processing approach for the inhomogeneous areas, “Local Method”

## Slide 20
Plenty of excellent
Empirical/ experimental
results in the literature
Some real life examples

## Slide 21
Ludeno, G., Reale, F., Raffa, F., Dentale, F., Soldovieri, F., Carratelli, E.P., Serafino, F. Integration between X-Band Radar and Buoy Sea State Monitoring (2018) Journal of Coastal Research

## Slide 22
Typical values of the parameters
Antenna rotation period influences accuracy of time FFT
Interval between pulses influences space resolution
Resolution is howvere good enough- Unlike…

## Slide 23
Proof of feasibility of the sea state monitoring from data collected in medium pulse mode by a X-band wave radar system
Ludeno, G., Raffa, F., Soldovieri, F., Serafino, F.
Remote Sensing, 2018,
Pulse duration of about 50 ns) at 9.5 GHz (X-Band) and the pulses are transmitted and received in the horizontal plane (HH polarization).
Pulse length:
To us just a technicality

## Slide 24
Radar Bathymetry
Echo-Sounder Bathymetry
Bathymetry map (Salerno harbour)

## Slide 25
Reflected waves from the jetties
Ludeno, G., Natale, A., Lugni, C., Soldovieri, F., Serafino, F. Remocean: A X-band radar system as tool for environmental monitoring in costa concordia ship wreck management (2014) 7th European Workshop on Structural Health Monitoring, EWSHM 2014 - 2nd European Conference of the Prognostics and Health Management (PHM) Society,

## Slide 26
Geometrical scheme of the tilt modulation and the shadowing effect. A typical microwave image of a sea wave field (dark and bright areas)
The shadowing phenomenon: no reflection from sea spots that are not in the line of sight (Plant and Keller 1990, Lee et al. 1995, Wenzel 1990) can provide a useful tool to extract information from the radar image
Extracting more information:
Shadowing

## Slide 27
SHADOWING
For a simple monocromatic wave:
More of it later!

## Slide 28
Chart: 
SHADOWING
On a «real» sea
(onedimensional)
Depends on grazing angle
Thus
Antenna height and distance
(so it changes along the radar field)
Has to be computed for each single wave

## Slide 29
Estimating SWH
Shadowing
Real SHADOWING
(2d)
Image
Shadow
Of course,
The algorithm is complex
but it can be tackled

## Slide 30
Illumination ratio as a function
of grazing angle and look
direction => SWH
For instance: R. Gangeskar (2014)
An Algorithm for Estimation of Wave Height From Shadowing in X-Band Radar Sea Surface Images
IEEE Transactions on Geoscience and Remote Sensing
Sea state
Doesn’t seem to be fully satisfactory
Possibly, can be integrated
with Spectrum/MTFapproach

## Slide 31
The most promising trick!
Extracting more information:
Doppler, «Coherent»

## Slide 32
Horizontal component of water particle velocity (Airy theory, drawing not in scale)
Vr≃ Vx Horizontal component
of the surface particle
(grazing angle)
(Hauser et al. 2005, Chen et al. 2017, 2019, Horstmann 2021
Hwang, P. A., M. A. Sletten, and J. V. Toporkov (2009), A note on Doppler processing of coherent radar backscatter from the water surface: with application to ocean surface wave measurements, J. Geophys. Res., doi:10.1029/2009JC005870 (in press).
The surface orbital velocity of water particles can be exploited to measure the sea state
For a simple monocromatic wave:
Incoming wave , fo is
backscattered with a modified
Frequency fo+-Δf
+ if Vr towards the source
- If Vr away from the source

## Slide 33
So, if a radar can measure the frequency of the reflected EM waves, it will also measure the Vr
and since Vr≃ Vx, there is a connection with the wave height H, and with SWH as well
Vz(x,t)=Hωsin(kx-ω t)
Vr of course varies along the surface , so what we find is a frequency distribution
of the (reflected) E/M energy as a function of (Doppler spectrum).
A correlation can thus be established between and the Doppler Spectrum E( )
…at least in theory.
Do not forget, however, that some particles are shadowed by the previous wave
Yes, very much
Like in HF system.
Less messy, though,
since Bragg is not
Interfering
So, you don’t get
«first» and «second»
order spectra

## Slide 34
Chart: 
SHADOWING
Plays a role here, too
Shadowing changes according to antenna elevation/distance
And wave spectrum

## Slide 35
According to the transformation seen earlier (Airy waves)
water elevation spectrum Sη is related to the velocity spectrum Su
And therefore to the doppler spectrum E( )
For a real non-monochromatic sea, the problem is complicated-
But it can still be managed
Vz(x,t)=Hωsin(kx-ω t)
Toporkov and G. S. Brown, "A numerical study of backscattering from time-evolving sea surfaces: comparison of hydrodynamic els," in IEEE Transactions on Geoscience and Remote Sensing, vol. 39 2001, doi: 10.1109/36.964977.
)

## Slide 36
Chart: 
Chart: 
| -0.4 | -0.34300000000000003 | -0.28599999999999998 | -0.22900000000000001 | -0.17199999999999999 | -0.115 | -5.8000000000000003E-2 | -1E-3 | 5.6000000000000001E-2 | 0.113 | 0.17 | 0.22700000000000001 | 0.28399999999999997 | 0.34100000000000003 | 0.39800000000000002 | 0.45500000000000002 | 0.51200000000000001 | 0.56899999999999995 | 0.626 | 0.68300000000000005 | 0.74 | 0.79700000000000004 | 0.85399999999999998 | 0.91100000000000003 | 0.96799999999999997 | 1.0249999999999999 | 1.0820000000000001 | 1.139 | 1.196 | 1.2529999999999999 | 1.31 | 1.367 | 1.4239999999999999 | 1.4810000000000001 | 1.538 | 1.595 | 1.6519999999999999 | 1.7090000000000001 | 1.766 | 1.823 | 1.88 | 1.9370000000000001 | 1.994 | 2.0510000000000002 | 2.1080000000000001 | 2.165 | 2.222 | 2.2789999999999999 | 2.3359999999999999 | 2.3929999999999998
VELXDEP.2 | 2 | 6 | 16 | 22 | 46 | 61 | 106 | 178 | 225 | 270 | 362 | 348 | 399 | 435 | 397 | 448 | 385 | 376 | 352 | 340 | 286 | 259 | 221 | 177 | 172 | 140 | 108 | 94 | 75 | 70 | 64 | 55 | 35 | 31 | 28 | 15 | 20 | 10 | 13 | 7 | 4 | 4 | 7 | 3 | 6 | 1 | 1 | 1 | 0 | 1
VELXDEP.1 | 3 | 11 | 14 | 42 | 49 | 89 | 145 | 184 | 261 | 333 | 384 | 441 | 410 | 472 | 484 | 459 | 426 | 420 | 356 | 367 | 311 | 266 | 247 | 205 | 180 | 153 | 123 | 102 | 82 | 76 | 72 | 53 | 36 | 41 | 27 | 17 | 23 | 11 | 10 | 10 | 5 | 3 | 6 | 5 | 6 | 1 | 1 | 1 | 0 | 1
VELXDEP.5 | 1 | 1 | 2 | 6 | 10 | 25 | 34 | 49 | 84 | 115 | 141 | 226 | 258 | 264 | 293 | 309 | 310 | 318 | 311 | 254 | 250 | 212 | 171 | 165 | 134 | 113 | 86 | 73 | 77 | 65 | 50 | 37 | 35 | 29 | 18 | 19 | 16 | 8 | 10 | 7 | 2 | 5 | 8 | 1 | 6 | 1 | 2 | 0 | 0 | 1
VELX | 1 | 0 | 5 | 6 | 10 | 9 | 22 | 26 | 36 | 58 | 106 | 105 | 164 | 217 | 271 | 371 | 425 | 514 | 597 | 728 | 843 | 905 | 985 | 950 | 985 | 1054 | 1005 | 896 | 886 | 787 | 692 | 620 | 516 | 406 | 318 | 239 | 175 | 129 | 102 | 74 | 50 | 32 | 19 | 17 | 6 | 11 | 7 | 2 | 1 | 1
Histogram of Vx occurences
Histogram of Vx=Vr occurences
taking shadowing into account
DEP.1 .2 .3 etc: degree of shadowing
Vx=~Vr , grazing angle
Vx is easily related to
=fo Vr/C
Simulated!
Note asimmetry
Depends on shadowing
(and direction of waves
If you introduce
Shadowing effect

## Slide 37
So it is possible to move from E( ) to Sη …
thus gaining a more direct insight into the sea wave spectrum (no need of an empirical MTF!).
There are problems however
Need a radar that can measure the frequency of the backscattered wave (coherent radar)-Expensive.
The algoriths become more complicated in the presence of:
Highly spread spectrum
Two or more peaks of the spectrum. (Swell, cross sea)
Strategies have to be developed in order to overcome these problems

## Slide 38
pulse repetition 1 kHz, allowed to ± maximum radial Doppler speed of 8 m/s
pulselength of 50 ns,thus a range resolution of 7.5 m.
antenna a vertical beam opening of 21° and a width of 7.5 feet (2.3 m) resulting in an azimuthal resolution of about 1°
In detail:
hourly cycle starting with 10 min of rotational data, which were utilized to retrieve the wave spectra and in particular the peak wave direction [3].
After these acquisitions the antenna is oriented into the radar-retrieved peak wave direction (looking up-wave) to acquire the Doppler spectrum (“static measurement”)
Retrieve spectrum peak direction (Non Doppler mode )
Orient the antenna into the radar-retrieved peak wave direction
(looking up-wave) to acquire the Doppler spectrum
Ruben Carrasco, Jochen Horstmann, and Jörg Seemann Significant Wave Height Measured by
Coherent X-Band Radar IEEE TRANSACTIONS ON GEOSCIENCE AND REMOTE SENSING, VOL. 55, NO. 9, 2017
To obtain stable Doppler velocities, the radar has to observe the same points over a relatively long time period. This is achieved by pointing the radar antenna into the peak wave direction, which will only allow to measure the orbital velocity component in the radar look direction. Then, the directional wave spectrum is retrieved from the radar data acquired with rotating antenna
A possible way- Carrasco et al
Locate direction on image- then Doppler on the peak direction

## Slide 39
Carrasco et al 2017

## Slide 40
J. T. Johnson, J. V. Toporkov and G. S. Brown, "A numerical study of backscattering from time-evolving sea surfaces: comparison of hydrodynamic models," in IEEE Transactions on Geoscience and Remote Sensing, vol. 39, no. 11, pp. 2411-2420, Nov. 2001, doi: 10.1109/36.964977.
By the way, we did not mention the
polarization issue:HH,VV, HV..
Maybe later.
Paul A. Hwang,1 Mark A. Sletten,1 and Jakov V. Toporkov1 A note on Doppler processing of coherent radar backscatter from the water surface: With application to ocean surface wave measurements
Note: asimmetry
Difference from
Linear model

## Slide 41
Horstmann, J., Bödewadt, J., Carrasco, R., Cysewski, M., Seemann, J., & Streβer, M. (2021). A coherent on receive x-band marine radar for ocean observations. Sensors, 21(23) doi:10.3390/s21237828
9.4 GHz pulse length 50 ns pulse rep freq up to 2000
Rotatio 1- 2 rps ris ang .012 range res 7.5 m altezza 43 m
VV «much better»
Data processing on the received
signal provides Doppler information
With a non- coherent radar
Note asymmetry

## Slide 42
FMICW(Frequency Modulated Interrupted ContinuousWave) operating frequency of MORSE ranges from 2.75 GHz to 2.95 GHz about 10 cm wavelength. (S Band )
Chen Z., Wang Z., Chen X., Zhao C., Xie F., He C. (2017). S-Band Doppler Wave Radar System. Remote Sensing 9, 1302
six horn antennas with each beam width of 30
FMICW(Frequency Modulated Interrupted ContinuousWave) operating frequency ranges from 2.75 GHz to 2.95 GHz about 10 cm wavelength. (S Band )
Range 0.01–0.5 Hz, 0–360
Resolution (freq) 0.01 dir Hz/10°
Update Time 2.5 min
Range Resolution 5/7.5/15 m Variable
Detecting Range 5 km
Polarization VV Wavelength 10.5 cm
Another possible way:many antennas
Chen et al-
MORSE

## Slide 44
Only commercially available Doppler wave radar
MIROS, C band (5.8 MHz)
daHauser et al2005
No information available

## Slide 45
K-band (SRK) radars with a frequency band 18-27 GHz ( wl 0.016-0.01) are being experimented for sea state monitoring. These systems have small coverage range (e.g. 100-300 m), but high temporal and spatial resolution, small size, and low weight. They are thus useful to analyse sea waves near the coast or in semi-closed areas (e.g. bays, harbours).
Ludeno, G., Catapano, I., Soldovieri, F., Gennarelli, G. Retrieval of Sea Surface Currents and Directional Wave Spectra by 24 GHz FMCW MIMO Radar (2023) IEEE Transactions on Geoscience and Remote Sensing, 61, art. no. 5100713, .
«Small is beautiful»
Very short wavelength, very short range
Emitted power | +18 dBm
Elevation beamwidth | 12.8°
Azimuth beamwidth | +/- 75°
Maximum range | 300m
Range resolution | 0.6m
Azimuth resolution | 7° (@0°) 13°(@75°)
Alimentazione | USB
Size | 13 x 11 (cm)
Weight (radar + case) | 410 g
radome/case | waterproof
On a different tack
(Ludeno et al. 2023, J. Cui et al. 2019).
Remember: short wl
Better resolution
Lower range
Affected by rain

## Slide 46
The antennas have horizontal and vertical beam widths of 30 degrees and 25 degrees, and each of them covers an angle of 30 degrees. A single antenna requires 3 min to collecting data; therefore, the total time required for a full directional wave height spectrum is 18 min.
Preliminary result show a significant accuracy in the measurement of SWH. However, the results of the average wave period, especially for a low sea state, are not satisfying. Yet.
Ludeno, G., Catapano, I., Soldovieri, F., Gennarelli, G. Retrieval of Sea Surface Currents and Directional Wave Spectra by 24 GHz FMCW MIMO Radar (2023) IEEE Transactions on Geoscience and Remote Sensing, 61, art. no. 5100713, .
Doppler is being considered

## Slide 47
Ludeno, G., et al Retrieval of Sea Surface Currents and Directional Wave Spectra by 24 GHz FMCW MIMO Radar (2023) IEEE Transactions on Geoscience and Remote Sensing, 61, art. no. 5100713
«Small is beautiful»
Very short wavelength, very short range
Low sea state at molo San Vincezo (Napoli)
Sea surface current map
Directional spectra:

## Slide 48
Briefly summarizing about MW wave radar
Reasonably low cost
Good reliabiliy once properly calibrated and tested
But
Sensitive to rain/hail (X Band)
New promising development (Doppler)